Product Specification

Personal GPS tracking device

CE-P8

- Applications

1. Vehicle rental / Fleet management etc 
2.Outdoor sports 
3. Protect children / elder/ Asset/ pet and so on 
4. Provide peace‐of‐mind for businessmen 
5. Personnel Management  
6.Criminals Tracking

2. Main Feature:

1. Online web platform, the historical and current location can be checked.

2. E-fence function.

3. Hijack alarm, 9 SOS numbers can be preset.

4. Remote voice monitoring.

5. Low battery alarm.

6. Inlayed 3D accelerator，moving and static state, energy smart.

7. Change the time interval of uploading automatically according to the speed.

8. Admin checks the altitude and longitude and location information by texting.

9. A-GPS solutions，shorter locating time，higher precision.

10. Long Duration battery up to 48 hours fully working ( test under updating per 30 seconds).

11. Sleep model ,5000MAH battery, can work 20 days .

3, Specs:

| Content | Specs. |
| --- | --- |
| Dim. | 105mm x 60mm x 20mm |
| Weight | 144g |
| Network | GSM/GPRS |
| Band | 850/900/1800/1900Mhz |
| GPS chip | UBLOX |
| GPS sensitivity | -159dBm |
| GPS accuracy | 5m |
| Time To First Fix | Cold status 35-80s Warm status 35s Hot status 1s |
| Car charger | 12—24V input 5V output |
| Wall charger | 110－220V input 5V output |
| Battery | Chargeable changeable 3.7V 1000mAh Li-ion battery |
| Standby | 240hours |
| Storage Temp. | -40°C to +85°C |
| Operation Temp. | -20°C to +55°C |
| Humidity | 5%--95% non-condensing |